## Slide 1: Penumbra: day-ahead solar forecasts that know when they're unsure
Calibrated probabilistic forecasting for Belgium's 12.1 GW PV fleet, benchmarked against the grid operator — DataNova 2026 · Sustainability · DN-SU-01
Adrian Issac Mamani Quispe · Arequipa, Peru
Live demo: https://skkippie.me/penumbra-solar-forecast/
Notes: Penumbra forecasts tomorrow's Belgian solar output with calibrated uncertainty, and is scored against Elia's own operational forecast.

## Slide 2: Solar is now Belgium's largest day-ahead uncertainty
12.1 GW
installed PV, up from 9.1 GW
Elia monitored capacity, Apr 2024 → Oct 2026
335 MW
average hourly error of the TSO forecast
Elia D-1 11h, daylight hours, backtest period
1,539 MW
P99 shortfall to cover with reserve
hourly over-forecast, 99th percentile
Day-ahead positions close at 12:00 on D-1: every MW of forecast error is bought back in balancing, mostly from gas plants.
Point forecasts hide how sure they are. Reserves and trading need honest uncertainty — wide when skies are mixed, tight when clear.
Who needs it: TSOs and DSOs (reserve sizing), balance-responsible parties and aggregators (bidding), and grids in emerging solar markets that lack a TSO-grade forecaster.
Notes: The problem is DN-SU-01: forecast solar generation from weather and plant data to support grid stability and renewable planning.

## Slide 3: Three ideas, one daily forecast
1
Eight weather models, not one
ICON, GFS, ARPEGE/AROME, ECMWF IFS, HARMONIE (KNMI, DMI), GEM and ECMWF's AI model AIFS — combined per province and weighted by installed PV. Their disagreement is a feature.
2
Bands you can trust
LightGBM quantile regression (P10/P50/P90) + Mondrian conformal calibration per sun-elevation regime: the 80 % band covers ~80 % of hours at dawn, noon and dusk.
3
Proven in public
Hybrid mode also reads Elia's own 11:00 forecast (forecast combination). Every daily forecast is committed to git before market close and scored afterwards.
Everything runs on free public data and free infrastructure (GitHub Actions + GitHub Pages).

## Slide 4: Real, public, verifiable data — 2.5 years, hourly
Source | What we use | Licence
Elia Open Data (ods032 / ods209 / ods210) | Measured PV output, installed capacity, 11 provinces, 15-min; Elia's D-1 11h forecast with P10/P90 | Elia Open Data Licence
Open-Meteo Previous Runs API | 8 NWP models archived at fixed 24 h / 48 h lead; GHI, direct, cloud, temperature at 11 provincial points | CC BY 4.0
Energy-Charts (Fraunhofer ISE) + Elia ods134 | Day-ahead and imbalance prices — impact analysis only, never model input | CC BY 4.0 / Elia
22,409
hourly targets, none imputed
0.88 % missing hours dropped
12,273
daylight hours used for scoring
sun elevation > −2°
Quarter-hours → hours only when all four exist; numbers stored as text with decimal commas are parsed and validated.
Radiation fields re-labelled to the interval they describe (verified: correlation peaks at zero lag).
Installed capacity lagged 2 days; target = capacity factor, so 33 % fleet growth does not leak.

## Slide 5: Pipeline and the no-look-ahead rule
Ingest
Elia + 8 NWP models
11 provinces, hourly
Features
capacity-weighted irradiance, clear-sky index (pvlib), POA, model spread, spatial dispersion, trailing performance ratio
Model
LightGBM quantiles P10/P50/P90 (+ Elia 11h in Hybrid)
Calibrate
Mondrian conformal per sun-elevation regime, last 60 days
Deliver
GitHub Action 10:30 UTC → append-only log → dashboard
Honesty rules (unit-tested)
Strict setting uses weather runs issued 48 h before each hour — all available before Elia's D-1 11:00 forecast.
Rolling-origin backtest: refit every month, predict the next unseen month (19 months, 575 days).
Every method scored on the identical set of daylight hours; significance by Diebold–Mariano + block bootstrap.

## Slide 6: Ties the grid operator on accuracy, beats it on uncertainty
2.88 %
Hybrid nMAE (strict) — Elia 2.87 %
optimistic inputs: 2.74 % vs 2.87 %
29 %
narrower 80 % band than Elia's P10–P90
coverage 81.2 % vs 80.0 %
10.4 %
better Winkler interval score than Elia
pinball 0.919 vs 0.969
Chart: nMAE, % of installed capacity (strict, lower is better)
| Persistence (D-2) | Climatology | Linear NWP | Penumbra weather-only | Penumbra Hybrid | Elia D-1 11h
nMAE strict | 7.76 | 7.3 | 4.26 | 3.5 | 2.88 | 2.87
Weather-only Penumbra, from free data alone: 3.50 % (strict) / 3.08 % (optimistic) — 55 % better than persistence.
Hybrid vs Elia on point error: −0.2 % (strict, DM p = 0.98) and +4.6 % (optimistic, p = 0.01).
The gain is in uncertainty: same coverage, much tighter bands → less reserve held for the same risk.

## Slide 7: Calibration holds in every sky regime
Chart: % of hours inside the 80 % band (target 80 %)
| overcast | variable | clear
Elia P10–P90 | 62.3 | 85.4 | 80.9
Penumbra Hybrid | 89.3 | 80.8 | 80.2
Chart: Point error is equal: nMAE by regime, % of capacity
| overcast | variable | clear
Elia D-1 11h | 1.11 | 3.29 | 2.99
Penumbra Hybrid | 1.11 | 3.29 | 2.99
Regimes are defined from the forecast clear-sky index (known in advance). Elia's band is far too narrow when overcast and too wide when the sky is mixed; conformal calibration keeps Penumbra at or above 80 % in every regime while its average band is 8.9 % of capacity vs 12.5 %.

## Slide 8: Stable across 19 out-of-sample months
Chart: Monthly nMAE, % of capacity (strict)
| 2025-04 | 2025-05 | 2025-06 | 2025-07 | 2025-08 | 2025-09 | 2025-10 | 2025-11 | 2025-12 | 2026-01 | 2026-02 | 2026-03 | 2026-04 | 2026-05 | 2026-06 | 2026-07 | 2026-08 | 2026-09 | 2026-10
Elia D-1 11h | 3.38 | 2.97 | 2.46 | 2.64 | 3.28 | 3.66 | 3.11 | 2.29 | 2.25 | 2.36 | 2.9 | 2.87 | 3.34 | 2.77 | 2.75 | 2.33 | 3.01 | 2.83 | 3.19
Penumbra weather-only | 3.73 | 6.09 | 4.45 | 3.36 | 3.77 | 4.17 | 3.55 | 2.6 | 2.43 | 2.67 | 2.83 | 3.35 | 3.92 | 2.94 | 2.99 | 2.43 | 3.2 | 3.12 | 3.49
Penumbra Hybrid | 3.34 | 3.52 | 2.36 | 2.68 | 3.41 | 4.03 | 2.81 | 2.43 | 2.17 | 2.4 | 2.71 | 3.29 | 3.42 | 2.58 | 2.59 | 2.2 | 2.88 | 2.82 | 2.67
Chart: Example: 2026-10-15 (largest gain vs Elia), MW
| 07:00 | 08:00 | 09:00 | 10:00 | 11:00 | 12:00 | 13:00 | 14:00 | 15:00 | 16:00 | 17:00 | 18:00 | 19:00
P10 | 0 | 182 | 1087 | 2295 | 3272 | 3870 | 4226 | 4103 | 3250 | 1954 | 728 | 99 | 0
P90 | 0 | 356 | 2053 | 3873 | 5133 | 5669 | 6069 | 5867 | 5127 | 3392 | 1683 | 244 | 0
Hybrid P50 | 0 | 275 | 1475 | 2940 | 3960 | 4591 | 5033 | 4823 | 3947 | 2537 | 1092 | 105 | 0
Elia D-1 11h | 0 | 322 | 1861 | 3525 | 4652 | 5341 | 5708 | 5525 | 4659 | 3246 | 1572 | 231 | 0
Measured | 0 | 238 | 1360 | 2453 | 3213 | 3445 | 3366 | 3218 | 3071 | 2270 | 1136 | 152 | 0

## Slide 9: What the improvement is worth
445 MW
narrower average 80 % band
at today's 12.1 GW, same coverage
7.45 €/MWh
imbalance cost of forecast error
Elia's forecast: 7.71 €/MWh
3.2 M€/yr
lower imbalance settlement
whole fleet, price-taker illustration
Reserve sizing: a TSO dimensions upward/downward reserve from forecast uncertainty — a band that is narrower at equal coverage is directly less capacity held idle (mostly gas).
Trading: a balance-responsible party can bid the quantile that minimises its expected imbalance cost instead of a single number.
Honest caveat: the P99 hourly over-forecast is 79 MW worse than Elia's — concentrated in negative-price hours when PV is curtailed.
Assumptions are explicit (price-taker, hourly settlement); figures are orders of magnitude, not a market simulation.

## Slide 10: Feasible today, portable tomorrow
Runs in production now
Daily GitHub Action issues tomorrow's forecast at 10:30 UTC, before the 12:00 CET gate.
Append-only forecast log, scored automatically when Elia publishes actuals.
Static dashboard on GitHub Pages: no server, no cost, no API keys.
Full backtest reproduces in ~10 minutes on a laptop (download ~15 min).
Portable to data-scarce grids
Weather-only mode needs just a production history and free global NWP — no TSO forecast.
Peru's southern solar hub (Arequipa, Moquegua, Tacna) sits under the world's highest irradiance; COES dispatch data can replace Elia's.
Capacity-factor target and per-region weighting carry over to any fleet size.
Next: per-province forecasts for DSOs, intraday updates, curtailment-aware features from price forecasts.

## Slide 11: Live dashboard and verifiable track record
Tomorrow: fan chart with P10–P90 band next to Elia's forecast.
Live record: daily error vs Elia, coverage, issue timestamps.
Backtest: method comparison, monthly skill, calibration, significance tests.
Explorer: any of the backtest days, with shortcuts to the hardest ones.
Demo
https://skkippie.me/penumbra-solar-forecast/
Code
https://github.com/S-kkipie/penumbra-solar-forecast

## Slide 12: Limits, responsible use and team
Known limits
Target is Elia's upscaled estimate of the fleet, not metered totals.
Market-driven curtailment at negative prices is only proxied (weekend/holiday flag, trailing ratio).
Accuracy depends on weather-run freshness: 48 h- vs 24 h-old runs cost 0.4 pp nMAE (weather-only).
National aggregate only; per-province models are future work.
Responsible data use
Aggregate, non-personal public data under open licences; all sources credited; claims reproducible from the repo; no result is reported without its benchmark and confidence interval.
Team
Adrian Issac Mamani Quispe (Arequipa, Peru) — full-stack / AI engineer: problem framing, data pipeline, modelling, evaluation, live system, dashboard and documentation.