## Slide 1: Penumbra: day-ahead solar forecasts that know when they're unsure
Calibrated probabilistic forecasting for Belgium's 12.1 GW PV fleet, benchmarked against the grid operator — DataNova 2026 · Sustainability · DN-SU-01
Adrian Issac Mamani Quispe · Arequipa, Peru
Live demo: https://skkippie.me/penumbra-solar-forecast/
Notes: Penumbra forecasts tomorrow's Belgian solar output with calibrated uncertainty, and is scored against Elia's own operational forecast.

## Slide 2: Solar is now Belgium's largest day-ahead uncertainty
12.1 GW
installed PV, up from 9.1 GW
Elia monitored capacity, Apr 2024 → Oct 2026
335 MW
average hourly error of the TSO forecast
Elia D-1 11h, daylight hours, backtest period
1,539 MW
P99 shortfall to cover with reserve
hourly over-forecast, 99th percentile
Day-ahead positions close at 12:00 on D-1: every MW of forecast error is bought back in balancing, mostly from gas plants.
Point forecasts hide how sure they are. Reserves and trading need honest uncertainty — wide when skies are mixed, tight when clear.
Who needs it: TSOs and DSOs (reserve sizing), balance-responsible parties and aggregators (bidding), and grids in emerging solar markets that lack a TSO-grade forecaster.
Notes: The problem is DN-SU-01: forecast solar generation from weather and plant data to support grid stability and renewable planning.

## Slide 3: Real, public, verifiable data — 2.5 years, hourly
Source | What we use | Licence
Elia Open Data (ods032 / ods209 / ods210) | Measured PV output, installed capacity, 11 provinces, 15-min; Elia's D-1 11h forecast with P10/P90 | Elia Open Data Licence
Open-Meteo Previous Runs API | 8 NWP models archived at fixed 24 h / 48 h lead; GHI, direct, cloud, temperature at 11 provincial points | CC BY 4.0
Energy-Charts (Fraunhofer ISE) + Elia ods134 | Day-ahead and imbalance prices — impact analysis only, never model input | CC BY 4.0 / Elia
22,409
hourly targets, none imputed
0.88 % missing hours dropped
12,273
daylight hours used for scoring
sun elevation > −2°
Quarter-hours → hours only when all four exist; numbers stored as text with decimal commas are parsed and validated.
Radiation fields re-labelled to the interval they describe (verified: correlation peaks at zero lag).
Installed capacity lagged 2 days; target = capacity factor, so 33 % fleet growth does not leak.

## Slide 4: Pipeline and the no-look-ahead rule
Ingest
Elia + 8 NWP models
11 provinces, hourly
Features
capacity-weighted irradiance, clear-sky index (pvlib), POA, model spread, spatial dispersion, trailing performance ratio
Model
LightGBM quantiles P10/P50/P90 (+ Elia 11h in Hybrid)
Calibrate
Mondrian conformal per sun-elevation regime, last 60 days
Deliver
GitHub Action 10:30 UTC → append-only log → dashboard
Honesty rules (unit-tested)
Strict setting uses weather runs issued 48 h before each hour — all available before Elia's D-1 11:00 forecast.
Rolling-origin backtest: refit every month, predict the next unseen month (19 months, 575 days).
Every method scored on the identical set of daylight hours; significance by Diebold–Mariano + block bootstrap.

## Slide 5: Ties the grid operator on accuracy, beats it on uncertainty
2.88 %
Hybrid nMAE (strict) — Elia 2.87 %
optimistic inputs: 2.74 % vs 2.87 %
29 %
narrower 80 % band than Elia's P10–P90
coverage 81.2 % vs 80.0 %
10.4 %
better Winkler interval score than Elia
pinball 0.919 vs 0.969
Chart: nMAE, % of installed capacity (strict, lower is better)
| Persistence (D-2) | Climatology | Linear NWP | Penumbra weather-only | Penumbra Hybrid | Elia D-1 11h
nMAE strict | 7.76 | 7.3 | 4.26 | 3.5 | 2.88 | 2.87
Weather-only Penumbra, from free data alone: 3.50 % (strict) / 3.08 % (optimistic) — 55 % better than persistence.
Hybrid vs Elia on point error: −0.2 % (strict, DM p = 0.98) and +4.6 % (optimistic, p = 0.01).
The gain is in uncertainty: same coverage, much tighter bands → less reserve held for the same risk.

## Slide 6: What the improvement is worth
445 MW
narrower average 80 % band
at today's 12.1 GW, same coverage
7.45 €/MWh
imbalance cost of forecast error
Elia's forecast: 7.71 €/MWh
3.2 M€/yr
lower imbalance settlement
whole fleet, price-taker illustration
Reserve sizing: a TSO dimensions upward/downward reserve from forecast uncertainty — a band that is narrower at equal coverage is directly less capacity held idle (mostly gas).
Trading: a balance-responsible party can bid the quantile that minimises its expected imbalance cost instead of a single number.
Honest caveat: the P99 hourly over-forecast is 79 MW worse than Elia's — concentrated in negative-price hours when PV is curtailed.
Assumptions are explicit (price-taker, hourly settlement); figures are orders of magnitude, not a market simulation.

## Slide 7: Live dashboard and verifiable track record
Tomorrow: fan chart with P10–P90 band next to Elia's forecast.
Live record: daily error vs Elia, coverage, issue timestamps.
Backtest: method comparison, monthly skill, calibration, significance tests.
Explorer: any of the backtest days, with shortcuts to the hardest ones.
Demo
https://skkippie.me/penumbra-solar-forecast/
Code
https://github.com/S-kkipie/penumbra-solar-forecast

## Slide 8: Limits, responsible use and team
Known limits
Target is Elia's upscaled estimate of the fleet, not metered totals.
Market-driven curtailment at negative prices is only proxied (weekend/holiday flag, trailing ratio).
Accuracy depends on weather-run freshness: 48 h- vs 24 h-old runs cost 0.4 pp nMAE (weather-only).
National aggregate only; per-province models are future work.
Responsible data use
Aggregate, non-personal public data under open licences; all sources credited; claims reproducible from the repo; no result is reported without its benchmark and confidence interval.
Team
Adrian Issac Mamani Quispe (Arequipa, Peru) — full-stack / AI engineer: problem framing, data pipeline, modelling, evaluation, live system, dashboard and documentation.